## Slide 1
DMR 2010792
Dan Neumann, National Institute of Standards and Technology
Goals:
Reproducible data analysis and experimental optimization workflows for the user community via Jupyter Lab.
Experimental optimization of the neutron instrument, measurement, and sample to greatly reduce measurement times and increase data quality.
Complete:
NR and SANS data fitting using SASVIEW and Refl1d software [1] controlled from Jupyter notebooks.
Feature-complete experimental optimization for SANS/NR following previously published method [2].
Experimental Optimization for Neutron Reflectivity (NR)
and Small Angle Neutron Scattering (SANS)
Complete (continued):
Gaussian process-based experimental optimization replacing the slow grid search and supporting more parameters at a time.
Local Jupyter notebook deployment.
Future Goals:
Validation and refinement by CHRNS staff.
Remote deployment of Jupyter notebooks accessible for external users.
[1] SASVIEW and Refl1D were originally developed under NSF DMR-0520547.
[2] Treece, B. W. et al. Optimization of reflectometry experiments using information theory. Journal of Applied Crystallography 52, 47–59 (2019).
Optimal solvent contrast for two NG7-SANS measurements on silica nanospheres in acetonitrile solvent of different isotopic composition.
Information gain (bits)
Optimal cuvette thickness for a 2.5 mg/mL lysozyme in D2O measurement at NG7-SANS.
(cm)